Ceramic filter

Ceramic filter is made by diatomaceous earth. It can remove harmful bacteria such as E. coli, Fecal Coli form, Salmonella, Streptococcus, and cysts (Cryptosporidium, Guardian). Reduces bad taste and odor, sediment, and asbestos. Cartridge is washable up to 30 times. The flow rate of the ceramic filter can be easily renewed by simply brushing its outer surface with a stiff toothbrush, plastic brush or soft scouring pad under running water. As the top layer of ceramic and contaminants are brushed off, a new layer becomes available. Do not use soap, detergents or steel wool.

Ceramic &Carbon filter

Plus Coconut Activated Carbon on basis of Ceramic filter, it not only remove harmful bacteria but also chlorine and cancer causing organic compound, heavy metal and mustinessand pesticide. It is the first filter which combination ceramic filter with coconut shell carbon filter.

Specification

| Materials | diatomaceous earth and coconut shell activated carbon |
| --- | --- |
| Diameter | OD. Φ 53--70mm，ID. Φ 28mm (or as per your requests)) |
| Lengths | 10 inches (or as per your requests) |
| Removal Ratings | 0.2-0.5micron |
| Service life | 6 - 12 months or about 12 metric tons of water |

Features

• Remove Cryptosporidium about 99%

• Reduces Giardia and other cysts about 99%

• Removes guinea worm

• Reduces Turbidity

• Ideally suited for application where mains pressure is low or gravity filter applicaions.

• Service life: 6 - 12 months or about 12 metric tons of water

Clean method

Clean the surface of ceramic filter with soft brush or scotchbrite pad under running tap water when the filter

has yellow color or when the flow rate has been decreased, but never use detergent.

# Text boxes

AIMER INDUSTRIAL CO.,LTD